MicroCore Labs

MCL51

Datasheet

Document Versions

1.0	5/2/2016	Initial version

Introduction

The MCL51 is an 8051 compatible embedded processor core that utilizes a high performance 32-bit microsequencer. It has an ultra-small footprint and can be highly customized.

The core is divided into the Execution Unit (EU) and the Bus Interface Unit (BIU). The EU is delivered in encrypted verilog and contains logic related to the microsequencer. The BIU is delivered as verilog source code and contains the SFRs and peripherals which allows the user to customize these components to their designs.

The signals between the EU and BIU are synchronous to the CORE_CLK and the EU communicates with the BIU using Strobes which it will assert to perform functions such as updating registers and enable/disable interrupts. No response from the BIU is required.

The MCL51 is delivered an example BIU interface that contains a UART, timer and interrupt controller. The UART has the ability to sense and load Intel-Hex format code into Program ROM.

Differences between MCL51 and original 8051

The MCL51 is 100% compatible with the 8051 instruction set but because it is a soft IP core it has some hardware differences between it and the original 8051.

The MCL51 does not have any pre-defined Parallel Port output pins which the original 8051 has accessable over P0 through P3 using SFR registers 0x80, 0x90, 0xA0, 0xB0.

The MCL51 does not have any External Memory mapped from 0x0000 to 0x00FF. External memory begins at 0x0100. This means that the MOVX instructions can not be used from addresses 0x0000 to 0x00FF. This was done to eliminate the additional hardware necessary to support these 256 memory locations.

The MCL51 utilizes a programmable vectored interrupt controller which allows the user to map up to 128 interrupt vectors into a table in Program Memory and the priorities of the interrupts are controlled in the BIU where they can be set by the user to any algorithm they need.

The peripherals such as the UART and Timers are not compatible with the original 8051. They are accessed using proxy addressing, use less logic, and are more flexible than the original peripherals. Sample peripherals with source code are supplied with the MCL51.

Signal Definitions

    input	CORE_CLK	// Global clock and reset
    input	RST_n

// EU to BIU signals
    output [7:0]	EU_BIU_ STROBE	// Strobe from EU
    output [7:0]	EU_BIU_DATAOUT	// Data to be written to BIU
    output [15:0]	EU_REGISTER_R3	// Target address to the BIU
    output [15:0]	EU_REGISTER_IP	// Instruction Pointer

// BIU to EU signals
    input [7:0]	BIU_SFR_ACC	// Accumulator SFR
    input [15:0]	BIU_SFR_DPTR	// DPTR SFR
    input [7:0]	BIU_SFR_SP	// Stack Pointer SFR
    input [7:0]	BIU_SFR_PSW	// PSW – Flags SFR
    input [7:0]	BIU_RETURN_DATA	// Data returned to the EU
    input	BIU_INTERRUPT	// Interrupt from the BIU

EU/BIU Communication

The EU communicates with the BIU over the EU_BIU_STROBE bus. This bus is asserted for as few as one clock and is used to command the BIU to perform reads and writes to RAM and ROM using multiple addressing modes. It is also used to globally enable or disable interrupts.

EU_BIU_STROBE[6:4]
0x0	= Program Code Space
0x1	= Direct Data Space
0x2	= Indirect Data Space

EU_BIU_STROBE[2:0]
0x0	= Idle
 0x1	= Write BIU_DATAOUT to address at EU_REGISTER_R3
0x2	= Read data addressed by EU_REGISTER_R3 into BIU_RETURN_DATA
0x3	= Global Interrupts Disable
0x4	= Global Interrupts Enable

Memory Mapping

The MCL51 supports the full 16-bit, 64KB range for both Program and Data memory. The example BIU includes 512 bytes of RAM and 4KB of program ROM. Increasing both to the maximum of 64KB can be done by directly connecting additional block RAMS or ROMS. Additional memory beyond the 64KB can also be added by implementing a custom memory paging system to the BIU using the SFR's.

One note: To avoid an additional multiplexed datapath in the core, “External” memory does not overlap “Internal” memory. “External” memory will begin at 0x100 and will not exist from 0x00 to 0xFF. The result is that using MOVX at addresses below 0x100 will map to the internal RAM using indirect addressing.

Memory Map:

0x0000 - 0x007F – 128 bytes of Direct/Indirect addressable RAM
0x0080 - 0x00FF – 128 bytes of Direct addressable registers used for the SFR's
0x0080 - 0x00FF – 128 bytes of Indirect addressable RAM used for scratch memory
0x0100 – 0xFFFF – Remaining 64KB of Data RAM addressed with MOVX and DPTR

Memory Block Note:

The MCL51 utilizes single-cycle, synchronous memory for the microcode ROM, Program ROM, and Data RAM. No pipelining should be used inside the RAM/ROM block or outside of it.
Bit-Addressable RAM

The MCL51 supports bit-addressable addressing across the 0x20-0x2F range as well as the SFR's that have addresses that are divisible by 8.

Special Function Registers – SFR's:

0x81	SP	Stack Pointer
0x82	DPL	DPTR - Data Pointer[7:0]
0x83	DPH	DPTR - Data Pointer[15:8]
0xA8	IE	Interrupt Enable
0xA9	*IS	Interrupt Source
0xC0	*PXY_DIN	Proxy Read Data
0xC1	*PXY_DOUT	Proxy Write Data
0xC2	*PXY_ADR	Proxy Address
0xD0	PSW	Program Status Word
0xE0	ACC	Accumulator
0xF0	B	B Register

* - Registers included in the MCL51 that are not part of the original 8051

0xA8 – IE – Interrupt Enable
Register contains the global interrupt enable bit which is the same as the original 8051.

IE[7] = Global Interrupt Enable

0xA9 – IS – Interrupt Source
Register contains seen bits of the interrupt source number which is sent by the BIU. Up to 128 unique interrupt sources are supported. This interrupt source will be multiplied by two which will create an address in code space that holds the address vector for that particular interrupt routine.

IS[6:0] = Interrupt Source

0xC0 – PXY_DIN – Proxy Read Data
Register contains the data that is generated by the selected peripheral.

0xC1 – PXY_DOUT – Proxy Write Data
Register contains the data that will be written to the selected peripheral. Writing to this register will initiate a write strobe to be sent to the addressed peripheral.

0xC2 – PXY_ADR – Proxy Address
Register contains the address for the peripheral. Writing to this register will initiate a read strobe to be sent to the addressed peripheral.

Proxy Peripheral Addressing

The MCL51 utilizes a proxy addressing method to access peripherals. This method reduces the load on the SFR's inside of the BIU and makes the interface more flexible.

Peripherals are connected to three SFR's. One for addresses, one for read data and one for write data. Upper bits in the PXY_ADR SFR are used to decode which peripheral is being accessed and to multiplex the data.

To write to a peripheral, first write the address to the PXY_ADR register. Then write the data to the PXY_DOUT register. This write will initiate the write strobe in the BIU to the peripheral which will complete the write cycle.

To read from a peripheral, first write the address to the PXY_ADR register. This will initiate a read strobe in the BIU to be sent to the peripheral. Then read the data back from the PXY_DIN registers.

Writes to the PDR_ADR register will always result in a read strobe being sent to the peripheral. It is suggested that peripheral registers should not have dual functions that would activate when a read strobe was received. Alternatively the read strobe may not be necessary to attach to the peripheral.

Interrupts

The MCL51 utilizes a low-latency vectored interrupt algorithm which is different from the original 8051. It allows for up to 128 unique interrupt sources with an interrupt vector table held in code ROM. The BIU prioritizes the interrupts and sends an interrupt source number to the EU for processing. The EU multiplies this number by two which becomes the address in code ROM that contains the address for the processing routine for that interrupt.

Interrupt Sequence

1)	BIU_INTERRUPT is received from the BIU
2)	At the end of the current instruction, the EU will disable interrupt globally and then read	SFR register 0xA9, the Interrupt Source register, and multiply it by two to create the	address in code ROM that holds the interrupt vector.
3)	The EU will fetch this vector from code ROM and perform an LCALL to this address

Inside the interrupt routine, the user should debounce the interrupt source so it will not be asserted upon exiting the interrupt routine.

At the end of the interrupt routine there should be an RETI instruction which will re-enable interrupts globally and return program execution to the address that was pushed to the stack. Like the original 8051, no other registers or flags are pushed to the stack so care should be taken to return the machine state back to the original condition before the interrupt routine was entered.

Like the original 8051, after returning from the interrupt routine, at least one instruction will be processed before the next interrupt is taken.

Interrupt vectors

Interrupt vectors are held in program ROM and contain two bytes for each interrupt source. Interrupt sources 0 and 1 should not be used as it would map to program ROM addresses 0x00 – 0x03 which already contain an LJMP that is executed right after RESET.

Interrupt vectors are stored in ROM with the upper byte of the vector held in the lower addresses.

For example:

INT2 =	Program ROM address 0x04 = Vector-2 address[15:8]
Program ROM address 0x05 = Vector-2 address[7:0]

INT3 =	Program ROM address 0x06 = Vector-3 address[15:8]
Program ROM address 0x07 = Vector-3 address[7:0]

MCL51 Integration into an FPGA

Integration of the MCL51 core is straightforward. The user only needs to supply a 1024 deep by 32 bit wide ROM to hold the EU microcode and a block of ROM and RAM for program ROM and data RAM. There are no PLLs, DLL's or other additional resources required by the core.

The supplied example BIU contains 4KB of Program ROM and 512 bytes of Data RAM. Peripherals include a UART, a dual-output Timer, and a simple interrupt controller.

Peripherals

UART – Fixed baud rate that can snoop the RX line to load Intel-Hex format code into Program ROM. Baud rate timer is built into the peripheral. An interrupt is asserted when a byte is received.

Registers:
0x0	WO	Rx_Byte	Reading this register clears the RX_HAS_BYTE bit
0x1	RO	Status	Bit[0]=TX_BUSY Bit[1]=RX_HAS_BYTE
0x2	WO	Tx_Byte	Writing sends the byte over UART TX

Loader:
UART snoops RX line for the '{' character which will half the CPU and enable the Loader
After the '{' character is entered, the Intel-HEX file may be sent over the RX line.
When complete, send the '}' character which will reset the CPU and begin running the new code.

The Loader will not verify the checksum of the Intel-Hex program file.

Timer – Dual 24-bit output, programmable timers. Timer-0 is a frequency generator and Timer-1 is a one-shot timer.

Registers:
0x0	WO	Timer-0 Count Max[23:16]
0x1	WO	Timer-0 Count Max[15:8]
0x2	WO	Timer-0 Count Max[7:0]
0x3	WO	Timer-0 Enable	Bit[0]=1=Enable Timer output

0x4	WO	Timer-1 Count Max[23:16]
0x5	WO	Timer-1 Count Max[15:8]
0x6	WO	Timer-1 Count Max[7:0]
0x7	WO	Timer-1 Enable	Bit[0]=1=Enable Timer output
0x8	WO	Timer-1 Debounce	Writing to register will debounce Timer-0 output

Timer-0 can be used to generate a constant square-wave frequency and Timer-1 can generate periodic interrupts to the CPU which need to be debounced.

EU ROM Description

The signals for the EU microcode ROM are described below. The ROM should be 1Kx32 with no registered outputs.

//---------------------------------------------------------
// EU Microcode ROM. 1Kx32
//---------------------------------------------------------

module eu_rom
  (
input	Reset,
input	OutClock,
input	OutClockEn,
input [9:0]	Address,
output [31:0]	Q
  );